## Slide 1
Oil Slick Characterization with UAVSAR
Cathleen E. Jones, Benjamin Holt
Jet Propulsion Laboratory, California Institute of Technology
Abstract ID: 254026
© 2017 California Institute of Technology. Government sponsorship acknowledged
AGU Fall 2017, Session 27022
References:
Jones, C. E., K.-F. Dagestad, O. Breivik, B. Holt, J. Rohrs, K. H. Christensen, M. Espeseth, C. Brekke, S. Skrunes (2016). Measurement and modeling of oil slick transport, J. Geophysical Res.-Oceans, 121, 7759-7775, doi:10.1002/2016JC012113.
Skrunes, S., Brekke, C., Jones, C., and Holt, B. (2015). A multisensor comparison of experimental oil spills in polarimetric SAR, IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, doi:10.1109/JSTARS.2016.2565063
Latini, D., Del Frate, F., Jones, C. E. (2016). Multi-frequency and polarimetric quantitative analysis of the Gulf of Mexico oil spill event comparing different SAR systems. Remote Sensing of Environment, 183, 26-42, doi:10.1016/j.rse.2016.05.014.
Fore, A. G., Chapman, B. D., Hawkins, B. P., Hensley, S., Jones, C. E., Michel, T. R., & Muellerschoen, R. J. (2015). UAVSAR Polarimetric Calibration. IEEE Transactions on Geoscience and Remote Sensing, 53(6), 3481-3491.
Minchew, B., Jones, C. E., & Holt, B. (2012). Polarimetric analysis of backscatter from the Deepwater Horizon oil spill using L-band synthetic aperture radar. Geoscience and Remote Sensing, IEEE Transactions on, 50(10), 3812-3830.
Jones, C. E., Minchew, B., Holt, B., & Hensley, S. (2011). Studies of the Deepwater Horizon oil spill with the UAVSAR radar. In Y. Liu et al. (Eds), Monitoring and Modeling the Deepwater Horizon Oil Spill: A Record-Breaking Enterprise (Geophys. Monogr. Ser., Vol. 195, pp. 33-50). Washington D. C.: American Geophysical Union.
2010: Deepwater Horizon Oil Spill,
Gulf of Mexico
2015: Norwegian oil-on-water exercise, North Sea
This work was carried out in part at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with NASA.
UAVSAR’S Unique Contribution: First quantitative measurement of oil:water volumetric fraction within a slick using SAR [Minchew et al., 2012]
2016: NOAA Oil slick study, Taylor Energy Seep, Gulf of Mexico
Airborne Synthetic Aperture Radar’S Advantages for Oil Spill Response and Assessment
Airborne instruments can have significantly higher power than satellite SARs, yielding much higher signal-to-noise ratio.
Extremely low noise instrument enables measuring radar-dark oil slick characteristics
Rapid repeat observations (up to 4 per hour) enable tracking of changes in slick location and extent
Effective oil spill response requires specific information about the slick’s characteristics:
Key Parameters:
Spill position
Extent
Transport (3D)
Thickness & volume
Oil-to-water ratio
Weathering
Slick type (mineral vs. look-alike)
SAR is routinely used for this
New SAR-based capabilities being studied & developed with UAVSAR
Parameter | Value
Center Frequency | L-Band @ 1.257 GHz
Bandwidth | 80 MHz
Intrinsic Resolution | 1.8 m Slant Range, 0.8 m Azimuth
Polarization | Full Quad-Polarization
Antenna Aperture | 0.5 m range/1.5 m azimuth
Azimuth Steering | Greater than ±20
Transmit Power | > 3.1 kW
Nominal Spatial Posting | 6 m
Range Swath | 22 km
Look Angle Range | 25º - 65º
Noise Equivalent sº | < -34 dB
Radiometric Accuracy | < 1 dB relative, 2 dB absolute
Radar
UAVSAR Instrument characteristics
Complex Permittivity
e = e' – ie''
Crude oil eO = 2.3 –i0.02
-Low conductivity surface
Sea water esw = 80 –i70
-High conductivity surface
Ocean Surface (no oil)
Ocean Surface
+Thin Sheen
Sheen
Emulsion
eSW = 80 –i70
-Reduced roughness
-Sheen too thin to
change esw
-New dielectric layer
with e mixture
–Alters scattering
eSW+Sheen ~~ 80 –i70
Emulsion =
Mixture of Oil
+ Sea water
eMixture = eSW + eO
-Frequency, temperature
dependent
Radar backscattered signal responds to volumetric fraction of emulsified oil as a mixture of oil and seawater
Characterization Of Oil Within Slicks Using SAR
UAVSAR’S Unique Contribution: Tracking the spreading and transport of different mineral oil slicks & a plant oil slick enabled improved modeling of oil transport in the ocean, both on the surface & in the water column [Jones et al., 2016].
PLANT OIL
Rapidly entrains
Most oil stays below surface
Reservoir of resurfacing oil
Less wind-driven transport
80% OIL EMULSION
Slowly entrains
Most oil stays at surface
Stronger wind-driven transport
Simulation Start Time: 05:48
Photos taken over the slick on 6/23/2010 between 16:00 and 20:00 UTC (NOAA RAT-Helo and EPA/ASPECT)
N
wind
Oil concentrated along wind rows:
Covered main slick & Gulf coastline
2 days, 3 flights, 21 flight hours
Imaged an area of 120,000 km2
Deepwater Horizon Spill, 2010
Gulf Ecosystem Impact & Recovery, 2010-2012
Norwegian Oil-on-Water Exercise, 2015
Gulf of Mexico NOAA Experiment, 2016
Repeated yearly observations
Focused on heavily oiled marshlands
Track long-term ecosystem response
Controlled experiment
Release known volumes & mixtures
Measure & model 3-D slick transport
Engage with U.S. response & recovery
Measure release from an abandoned rig
Measure extent, relative thickness, volume, weathering
UAVSAR’S Unique Contribution: Fine spatial resolution map of relative oil thickness derived from contrast between slick and clean water using VV-polarization returns.
~20 km
UAVSAR image of the Taylor Energy Slick
(VV-polarization)
Oil classification – relative thickness like the Bonn classification
Based on the VV damping ratio
Transport & Weathering
(shows the oil that was on surface for the longest time)
1
2
3
4
Transport path